## Slide 1: Introduction to the GPGPU (General-purpose computing on graphics processing units) and to OpenCL
Prof. Dr.-Ing. Andreas Maier, Prof. Dr.-Ing. Dietmar Fey
Jessica Magaraggia, Martin Berger, Frank Schebesch
Notes: Reminding the truth

## Slide 2: Outline
Background and history
Overview of the graphic pipeline
GPGPU architecture
Cuda
OpenCL
OpenCL example

## Slide 3: GPGPU – General Purpose Graphics Processing Unit
Graphics cards: Short background
  Original use: Control of the PC‘s monitor by means of the graphics cards
  Middle of the 80es: Graphics cards with 2D-acceleration
  Beginning of the 90es: First 3D-Acceleration

## Slide 4: GPGPU – Introduction (1)
At the beginning, no standard programming interface was available
Early 90es:
  Establishment of OpenGL in the professional context
  The fast development lead to successful spread in the market shares
End of the 90es:
  Graphics cards take over in the context of coordinate transformations and of Illumination (e.g. NVIDIA GeForce 256)
  The term Graphics Processing Unit appears in the scientific community
2000es: Shader-Programming ( Pixel-Shaders and Vertex-Shaders are used for graphic rendering)
Nowadays:
  Graphics cards manufacturers: ATI und NVIDIA
  High demand on the market → low prices

## Slide 5: GPGPU – Introduction (2)
Summary of the graphics cards‘ development:
VGA Controller Memory Controller Display Generator
GPU (Graphics Processing Unit) The Processing of the traditional graphic pipeline
GPGPU (General Purpose Graphics Processing Unit) Programmable processors replaced fixed function blocks Increased computational accuracy Parallel programming is required → CUDA

## Slide 6: OpenGL – Graphic Pipeline
Shader
  It is the program in charge of the shadowing
  It acts on junction points, (vertices), on geometric primitives (vertices, lines, triangles, etc.) and single points in the image
  Some units are programmable (blue), some are hardwired (white)
Textures
  They describe characteristic of the points on a surface
  Interpolation is done on floating points
  Often disregarded in 1D, 2D- oder 3D-fields
Notes: Vertex Shader: transformiert die 3D Position eines Knotens auf den 2D Schirm. Geometrie Shader kann geometrische Primitive in die Szene einfügen und herausnehmen. Setup und Rasteriserungseinheit erzeugt Pixelfragmente für ein geometrisches Primitiv. Pixel Shader greifen häufig auf Texturen zu, die Musterungen von Objekten beschreiben.

## Slide 7: GPGPU – Architecture (1)
General configuration of a GPGPU

## Slide 8: GPGPU – Architecture (2)
Hierarchy of the memory of a GPU:
  Global memory
    Located in an external DRAM
    Not explicitly accessible by a CUDA-program
    Accessible just by a thread at a time
  Shared memory
    Located in specific SRAM-banks
    SM-specific
Notes: Textur-Prozessor-Cluster Heterogene Multikern-Architekturen

## Slide 9: GPGPU – Architecture (3)
  Local memory
    Thread-specific
    Located in external DRAM
    Configurable
  Special memory
    Textures
    Constants
  Both local and special memory are of type constant. They are writable by the CPU at the beginning of the computation on the graphics card

## Slide 10: GPGPU – CUDA-Programming Model
CUDA supports:
  Parallel threads
  Programming schemas with parallel data
Difference w.r.t. other parallel threads approaches:
  All threads need to perform the same operation
  In this context we talk of data parallelism
  Nvidia refers to this schema as: SIMT (Single Instruction Multiple Threading)
Nevertheless it is possible to switch between threads of a specific thread field during an application

## Slide 11: OpenCL Platform
The OpenCL platform includes several components
  One Host (CPU-based)
  Compute Devices (GPU)
  Compute units ( groups of execution and arithmetic units)
  Processing elements (executing OpenCL Kernels)
Serial code executes in the Host
Parallel code executes in the Compute devices
Processing Element
Compute Device
Compute unit
HOST
Woolley2011
Notes: Compute Units” (akin to execution units & arithmetic processing unit groups on multi-core CPUs - think “cores”)
At the lowest level, these processing elements all execute OpenCL “Kernels

## Slide 12: OpenCL: How the execution works
Notes: The Host is run by the application. On the host side, blocking API functions can perform
waits for certain events to complete, such as all events in the queue
to finish, specific events to finish

## Slide 13: OpenCL Kernels
An OpenCL Kernel represents the code executed by a Work item
Kernels process in parallel: their execution needs to be independent from one another
The code executed by the kernels needs to consider the required memory access

## Slide 14: Example of an OpenCL Kernel
Standard loop: The same code is repeated serially, one element after the other
OpenCL kernel: The same code is executed at each point in the domain in parallel

## Slide 15: Work Domain 1D
Global size: 20
Local size of the working group: 8
Vector a
Working item
get_global_id(0) = 8
Vector a
Working group

## Slide 16: Work Domain in 2D
Example: Point-wise image processing
The image represents the global dimension of the working domain (16 x 20)

## Slide 17: Work Domain in 2D (2)
The global domain is divided into work items (e.g. a pixel)

## Slide 18: Work Domain in 2D (3)
The global domain is divided into work items (4 x 4)
Work items are grouped in work groups which execute together
The work domain can be in practice bigger than the real size of the image
  It needs to be a multiple of the worksize

## Slide 19: Example of a GPU class (1)
We want to write a class that uses our addition kernel:
Code used with courtesy of Martin Berger

## Slide 20: Example of a GPU class (2)
Code used with courtesy of Martin Berger

## Slide 21: Example of a GPU class (3)
Code used with courtesy of Martin Berger

## Slide 22: References
Woolley2011: http://www.cc.gatech.edu/~vetter/keeneland/tutorial-2011-04-14/06-intro_to_opencl.pdf
Khronos2010: https://www.khronos.org/assets/uploads/developers/li-brary/overview/OpenCL-Overview-Jun10.pdf
Smith2013: http://www.cs.bris.ac.uk/home/simonm/workshops/Op-enCL_lecture4.pdf

## Slide 23: Questions?